## Slide 1
Cloud-Network Convergence in China Telecom
Yongqing Zhu
zhuyq8@chinatelecom.cn
IETF120 Sidemeeting

## Slide 2: Motivation
Cloud and network are deployed and managed separately in China Telecom before 2016, therefore:
Cloud services can't be accessed easily due to the non-standardized interfaces between cloud & network
Hard to provide integrated cloud & network services due to the separation of cloud & network
Low efficiency of operation and management due to the separation of cloud & network
Hard to expand Telecom Cloud services due to the coupling of network & services
Limited flexibility in service development and deployment due to the non-cloudified service anchor
Build cloud-network converged infrastructure to meet the increasingly serveice requirement...

## Slide 3: Cloud-Network Convergence Strategy of China Telecom
Building cloud-network converged infrastructure to offer diverse, customized, reliable services to various customers
Chart: 
| a | b | c
列1 | 1 | 1 | 1
Cloud-Network
Convergence
Unified provision
Unified operation
Unified service
  Unified abstraction and encapsulation of cloud & network resources
  Unified scheduling and orchestration of cloud & network resources
  Unified deployment and delivery of cloud & network services
  Unified portal for providing cloud & network services
  Unified operation and management of cloud & network resources
  Unified end-to-end monitoring and maintenance of cloud & network services
Network
Cloudification
Capability
Openness
Service
Orchestration
AI
Media Stream
Storage
Automation
Edu
Service Provision
Infrastructure
Service Enablement
Computing, Networking and Storage
OSS
Virtualization Layer
Optical Network
Mobile
IP Network
Access
Satellite
IDC
Configuration
Management
Alerts and Logs
Management
Service E2E
Maintenance
Fault
Location
Resource
Allocation
…
AR/VR

## Slide 4: Status Quo of Network, Cloud and Services
IP Network: connection for clouds and services
  Contains IP MAN, IP Backbone, and IDC
Telecom Cloud: cloud services based on virtualized infrastructure
  Deployed in central cloud, core cloud, and edge cloud
Diversified services
  2H: HSI, IPTV, VoIP…
  2B: dedicated network, cloud access…
  2C: 4G, 5G…
All services are based on Telecom Clouds
All Telecom Clouds are based on IP network
MAN
IDC
Backbone
MAN
Home
Business
Mobile
Edge Cloud
Core Cloud
Central Cloud
Edge Cloud
Core Cloud
Home
Business
Mobile

## Slide 5: Overview of Cloudified IP MAN
“Building Blocks” Architecture: easy to expand & flexible to deploy
  Contains Metropolitan POD, Cloud-Network POP, and Exit Zone
Network and Service Decoupling: services not affected by network
  Overlay service: SRv6/EVPN-based (unified protocol stack)
  Underlay network: enhanced network capabilities, e.g. nested slices, iOAM
Network Element Cloudifying: agile deployment & enriched VAS
  Mainly focus on service anchor cloudification
Till now, Cloudified IP MAN has over 120 million fixed and mobile subscribers access, and 1000+ cloud resource pools connected
CPE
gNB
Super-Spine
Super-Spine
A-Leaf
A-Leaf
Backbone
Cloud-Network Brain
Exit Zone
Spine
Spine
Metropolitan POD
A-Leaf
A-Leaf
A-Leaf
A-Leaf
Spine
Spine
A-Leaf
A-Leaf
CPE
gNB
CPE
gNB
CPE
gNB
Metropolitan POD
B-Leaf
B-Leaf
Edge DC
vBRAS-UP
S-Leaf
S-Leaf
Cloud-Network POP
MEC
Edge Cloud
DCGW
Core DC
vBRAS-CP
S-Leaf
S-Leaf
Cloud-Network POP
VPC
Core Cloud
DCGW
IDC
S-Leaf
S-Leaf
Cloud-Network POP
VPC
Center Cloud
DCGW
Other
MANs

## Slide 6: Key Components of Cloudified IP MAN: Metropolitan POD
A-Leaf
A-Leaf
Spine
Spine
A-Leaf
A-Leaf
CPE
gNB
CPE
gNB
CPE
gNB
CPE
gNB
Metropolitan POD
S-Leaf
S-Leaf
Cloud-Network POP
DCGW
HPC
AI inference
…
Level-2 Edge Cloud
S-Leaf
S-Leaf
Cloud-Network POP
DCGW
AI inference
…
Level-2 Edge Cloud
S-Leaf
S-Leaf
Cloud-Network POP
DCGW
…
Level-1 Edge Cloud
AI training
HPC
East-west traffic for inter-cloud services
North-south traffic for cloud-access services
Based on Spine-Leaf architecture, enabling elastic network scaling and rapid traffic steering
  Easy to scale: Spine/Leaf can scale in/out per service demands w/o impacting network or services
  Full-mesh: Agilely steering the north-south and east-west traffic from clouds and subscribers
  Metropolitan POD can expand network capacity and enhance device capability to satisfy the increasing demands of AI/HPC services in the future

## Slide 7: Key Components of Cloudified IP MAN: Cloud-Network POP
Plug-and-Play, enabling fast and standardized cloud-network integration
  Pre-deployed infrastructure: connecting S-Leaf and DCGW within the Cloud-Network POP and allocating link bandwidth according to service demands
  Dynamic-deployed channel: dynamic configuring SRv6/EVPN between subscribers & services to enable rapid cloud service provision
Spine
Spine
DCGW
DCGW
vRouter
vRouter
vSwitch
vSwitch
vSwitch
vSwitch
VM
VM
…
VM
VM
…
Cloud-network POP
A-Leaf
A-Leaf
Metropolitan POD
Cloud
Subscribers
Cloud Services
EVPN over SRv6
S-Leaf
S-Leaf
overlay
underlay
VPC
IGP
EBGP
EBGP

## Slide 8: Unified Cloud-Network Scheduling
Integrating the management of cloud-network to optimize resource allocation and enhance scalability
A-Leaf
A-Leaf
Spine
Spine
Super-Spine
Super-Spine
Cloudified IP MAN
Edge Cloud
Core Cloud
CPE
gNB
Cloud-Network Orchestrator
3
1
2
Cloud-Network
Repository
Cloud-Network Controller
Network Controller
Cloud Controller
4
4
Cloud-network Brain
  If triggered, Orchestrator queries Repository for cloud and network resources
  Repository allocates physical resources (devices, ports, etc.) and logical resources (VLANs, slices, etc.) for services
  Orchestrator assigns configuration tasks to Cloud and Network Controllers based on allocated resources
  Controllers issue configurations to cloud and network respectively
2
4
1
3

## Slide 9: Service Anchor Cloudification
At first stage, mainly focusing on fixed broadband service anchor cloudification (C/U Separated vBRAS) to improve resource utilization and management efficiency
  vBRAS-CP (Control Plane device): fully cloudified
          Intensive management of user sessions, addresses, and other resources
  vBRAS-vUP (virtualized User Plane device): fully cloudified
          Carrying IPoE-based service (e.g. VoIP) to improve resource utilization
  vBRAS-pUP (physical User Plane device): high-speed forwarding device
          Efficiently forwarding the high-traffic services (e.g. HSI, IPTV)
In the future, building Unified Cloud Base for fixed and mobile services
  Cloudified UPF & Cloudified BRAS in the same framework
Till now, Cloudified C/U separated vBRAS accesses over 40 million HSI subscribers
* dBNG： disaggregated Broadband Network Gateway
Traditional
BNG
C/U separated vBRAS
vBRAS-pUP pool
vBRAS-CP
vBRAS-vUP
…
cloudified
dBNG
High-speed Forwarding Device
High-speed Forwarding Device
fully
cloudified
vBRAS-CP
vBRAS-UP
Future
UPF
Unified Cloud Base
…
Service Anchor Cloudification provides a platform for flexible service development and deployment

## Slide 10: Case 1: Smart Edge Cloud Service
Migrating home VAS into cloud w/o altering CPE and networking mode
  Establishing fast connections between homes and edge cloud based on Cloudified IP MAN
  Providing agile and diverse cloud services based on sunk edge cloud
  Migrating certain functions of CPE (e.g. DHCP, NAT) into cloud to construct intranet between home and cloud services
Expanding to IoT services in the future
ONU
Home Terminals
OLT
A-Leaf
Spine
Spine
Cloudified IP MAN
A-Leaf
SRv6/EVPN
Super-Spine
Super-Spine
Edge Cloud
App Market
Cloud Desktop
vCDN
Cloud Disk
VR/AR
……
S-Leaf
S-Leaf
Backbone
Internet Traffic
Cloud Access Traffic
DCGW
DCGW
Cloud-Network POP

## Slide 11: Case 2: Dedicated Network for Education Sector
Building high-quality education dedicated network based on Cloudified IP MAN
  Flexibly connecting sites and clouds based on SRv6/EVPN
  Providing customized channels for cloud/cloud connection and cloud/customer connection based on nested slices
  Deploying efficient multicast service among cloud/cloud and cloud/customer based on BIERv6
  Enabling visualized management for cloud-network services based on iOAM
Administration
Video Sharing
Courseware Sharing
Live Teaching
Level-2 Slice
Level-1 Slice
Cloudified IP MAN
BIERv6
S-Leaf
S-Leaf
A-Leaf
A-Leaf
OLT
Spine
Spine
S-Leaf
S-Leaf
A-Leaf
A-Leaf
OLT
OLT
Campuses
Campuses
EdTech Center
SRv6/EVPN+iOAM
Edu Cloud
Cloud Accessing
DCGW
DCGW
Education Apps
Live teaching
……
Cloud Disk
Security Suite
DCGW
DCGW
Edge cloud
OLT
Nested Slice

## Slide 12: Takeaway
Cloud-network convergence is successful in China Telecom, will keep pushing it forward
Cloudified IP MAN will play a more and more important role in Cloud-network convergence
Service anchor cloudification provides a platform for flexible service development and deployment
Next Steps
  Building Unified Cloud Base for fixed and mobile services
    Non-cloudified vBRAS-pUP limits the flexibility of service development and deployment
  Accelerating the process of standardizing resource interfaces
    Incomplete standardization of resource interfaces hinders unified service provision and management
  Expanding smart edge cloud service to IoT
  ……
There is a long way to go, let's push it forward together

## Slide 13
a
Questions and Feedback are Welcome

## Slide 14
a
Thanks!